## Slide 1
Topology-Preserving Segmentation
of Congenital Heart Disease
Cascaded nnU-Net with FiLM Disease Conditioning & soft-clDice Loss
nnU-Net V2 fork · all-experiments branch · Stanford / Akshay Lab
22
Composed Trainers
5
Mixin Features
8
Cardiac Labels
8
Disease Flags
1 / 14

## Slide 2
Motivation
Why do we need topology loss and disease conditioning?
2 / 14
~0.95
Whole-Heart Dice (3d_fullres baseline)
→ But two systematic failure modes remain:
Failure 1 — Great Vessel Label Confusion
◆ AO/PA label confusion in TGA & DORV cases
◆ Fullres patch lacks global context to determine which vessel exits which ventricle
◆ TGA: aorta exits RV, PA exits LV — reversed from normal anatomy
◆ DORV: both great vessels exit RV — both labels spatially ambiguous
Failure 2 — VSD Boundary Ambiguity
◆ VSD: inter-ventricular septum is absent or incomplete
◆ Model predicts single large LV region instead of LV + RV
◆ AVSD: all four-chamber septal borders ambiguous simultaneously
Our Solutions
◆ Cascade pipeline: low-res stage sees full cardiac anatomy in one patch → global context
◆ FiLM conditioning: inject disease vector to bias network toward correct anatomy
◆ soft-clDice topology loss: penalise broken vessel centerlines on AO & PA

## Slide 3
Data: Labels & Disease Flags
8 cardiac structures · K=8 binary disease flags per case
3 / 14
ID
Structure
Abbrev
Topo?
0
Background
BG
—
1
LV Blood Pool
LV-BP
—
2
RV Blood Pool
RV-BP
—
3
Left Atrium
LA
—
4
Right Atrium
RA
—
5
Myocardium
Myo
—
6
Aorta
AO
clDice ✓
7
Pulmonary A.
PA
clDice ✓
disease_map.json → {"SV_001": [0,0,1,0,0,0,0,1], ...}
Idx
Flag
Key implication
Topology risk
0
HLHS
LV may be absent/tiny; AO unreliable
Low
1
ASD
LA–RA may be adjacent
Low
2
VSD
LV–RV boundary ambiguous
VSD
3
AVSD
All 4-chamber borders ambiguous
AVSD
4
DORV
Both AO & PA exit RV
DORV
5
PuA
AO/PA fused — vessel absent
Low
6
ToF
Overriding aorta straddles VSD
ToF
7
TGA
AO↔RV, PA↔LV (reversed)
TGA ★

## Slide 4
Cascade Pipeline Architecture
Two-stage approach: global context → local boundary refinement
4 / 14
Stage 1 — 3d_lowres
◆ ~3–4 mm voxel spacing
◆ Full heart in every patch
◆ Global label assignment
◆ FiLM: disease-aware topology
◆ Optional: clDice on AO/PA
◆ Output → coarse labels
→
concat one-hot prior
→
Stage 2 — 3d_cascade_fullres
◆ ~1 mm voxel spacing
◆ Local boundary crop
◆ Prior from Stage 1 as extra channels
◆ FiLM: disease-aware refinement
◆ Optional: clDice on AO/PA
◆ Output → final labels
Key insight: Stage 1 sees the entire cardiac anatomy → correct global vessel assignment. Stage 2 sharpens boundaries using the Stage 1 prior + full resolution.
⚠ ExperimentPlannerForceLowRes required — default nnU-Net planner skips 3d_lowres for cardiac CT

## Slide 5
FiLM Disease Conditioning
Feature-wise Linear Modulation at the bottleneck
5 / 14
Image → Encoder → Bottleneck
↓
disease_mlp( vec_K8 ) → γ, β (channel-wise)
feature = (1 + γ) × feature + β
↓
Decoder → Segmentation
Bottleneck-only
Decoder has N=7 stages → (1+γ)^7 ≈ 2× feature distortion with γ=0.1. Applied at bottleneck only.
Near-zero init
weights σ=0.01 → identity transform at start. Training begins from unconditioned baseline.
LR × 2.0
disease_mlp + bottleneck_film params use 2× learning rate to learn conditioning faster.
CFG dropout 10%
10% of batches use zero disease vector. Prevents over-reliance on disease label at inference.
Instability Lesson (Early Experiments)
Applied FiLM at all 7 decoder stages →
(1 + γ)^7 ≈ 1.95× feature distortion at γ = 0.1
With LR×10 + momentum 0.99:
γ grew large fast → training diverged
Fix: bottleneck-only + LR×2 + near-zero init
Training is now stable across all experiments
disease_param_prefixes = {
'disease_mlp',
'bottleneck_film'
}

## Slide 6
Topology Loss: soft-clDice
Shit et al., CVPR 2021 — clDice: A Novel Topology-Preserving Loss
6 / 14
S. Shit et al. "clDice - a Novel Topology-Preserving Loss Function for Tubular Structure Segmentation." CVPR 2021.
Core Idea
◆ Standard Dice measures voxel overlap — insensitive to broken connectivity
◆ Two predictions with same Dice can have very different topology (one vessel vs many fragments)
◆ clDice: compare soft skeletons (centerlines) of prediction and GT
◆ A broken vessel → skeleton fragments → low skeleton overlap → high loss
◆ Fully differentiable — gradients flow through soft morphological operations
clDice Formula
tprec = Σ(skel_pred · gt) / Σ(skel_pred) ← skeleton inside GT
tsens = Σ(skel_gt · pred) / Σ(skel_gt) ← GT skeleton inside pred
clDice = 2·tprec·tsens / (tprec + tsens + ε)
loss = 1 − clDice
Applied as extra term: total = Dice+CE + w · clDice
Why Applied to AO (label 6) & PA (label 7) Only?
◆ AO and PA are tubular (vessel-like) — clDice designed for tubes
◆ Dominant failure modes (TGA, DORV) involve AO/PA topology
◆ Non-tubular structures (LV, RV, atria) do not benefit from skeleton loss
◆ Applying to all 8 classes × 10 skeleton iters would be computationally prohibitive
◆ Label IDs resolved dynamically from dataset.json keyword match
3D Implementation — Fully Supported
soft_erode / soft_dilate detect tensor dimensionality: 4D (B,1,H,W) → F.max_pool2d (kernel 3×3) 5D (B,1,D,H,W) → F.max_pool3d (kernel 3×3×3) No code changes needed for 3D — already dimension-agnostic.

## Slide 7
Soft Skeletonization Algorithm
Differentiable skeleton via iterative morphological opening
7 / 14
# Soft morphological primitives
def soft_erode(x): return -max_pool3d(-x, k=3, pad=1) # min-pool
def soft_dilate(x): return max_pool3d( x, k=3, pad=1) # max-pool
def soft_open(x): return soft_dilate(soft_erode(x)) # open = erode→dilate
# Iterative skeleton accumulation
skeleton = zeros_like(x)
current = x.clone()
for _ in range(num_iter=10):
opened = soft_open(current) # remove thin structures
skeleton += ReLU(current - opened) # residual = thin structures
current = soft_erode(current) # shrink further
return skeleton
Algorithm Properties
◆ Differentiable — gradients backpropagate through all pooling ops
◆ GT skeleton computed with torch.no_grad() (no gradient needed)
◆ num_iter=10 controls skeleton thickness (higher → captures thicker tubes)
◆ Kernel size fixed at 3 (3×3×3 in 3D) — smallest meaningful structuring element
◆ Memory: 10 × 2 pooling ops per class per batch → 2 classes (AO+PA) = 40 ops
How the skeleton accumulates across iterations:
iter 0
Full vessel mask
→
iter 3
Medial region only
→
iter 6
Near centerline
→
iter 9
Centerline voxels
→
∑ residuals
Soft skeleton
Accumulating residuals across all iterations produces a soft approximation of the morphological skeleton — the set of centerline voxels equidistant from the vessel boundary.

## Slide 8
Two Topology Mixin Variants
Fixed weight (existing) vs. Scheduled weight (new)
8 / 14
TopologyLossMixin (existing, all current trainers)
topo_weight = 0.2 (constant)
topo_num_iter = 10
topo_class_ids = [6, 7] (AO, PA)
Loss = Dice+CE + 0.2 × clDice
Applied from epoch 0 → topology loss active
immediately, even when predictions are random.
⚠ Risk: topology term may interfere with
Dice+CE convergence in early epochs.
TopologyLossScheduledMixin (new)
topo_warmup_epochs = 10 (0 → w_high ramp)
topo_decay_start = 40 (plateau ends)
topo_w_high = 0.5 (peak weight)
topo_w_low = 0.05 (final weight)
Epoch 0–9 : linear ramp 0.0 → 0.5
Epoch 10–39: plateau at 0.5
Epoch 40–99: cosine decay 0.5 → 0.05
✓ Dice+CE converges first (epochs 0-9)
✓ Topology enforced at peak (epoch 10-39)
✓ Gentle decay prevents over-constraint
Weight schedule over 100 epochs:
Warmup (0→10)
Plateau (10→40)
Cosine Decay (40→100)
←─────────────────── 100 epochs ───────────────────→
Both mixins share the same mixin_extra_loss() implementation (inherited from TopologyLossMixin). TopologyLossScheduledMixin only adds mixin_on_train_epoch_start() to update self.topo_weight each epoch using topo_weight_schedule().

## Slide 9
Composable Mixin Architecture
Feature modules stack via Python MRO — no monolithic subclassing
9 / 14
Available Mixins
DiseaseConditioningMixin
Injects disease vector via FiLM or MLP wrapper
TopologyLossMixin
Adds soft-clDice on AO/PA (fixed weight 0.2)
TopologyLossScheduledMixin
Like above but with warmup→plateau→decay schedule
CurriculumWeightsMixin
Per-class CE weights that evolve during training
Hook Dispatch Chain (each mixin calls super())
mixin_init()
Set mixin-specific __init__ attributes
mixin_initialize()
Post-setup: allocate GPU objects, resolve labels
mixin_extra_loss(...)
Return extra loss scalar to add to main loss
mixin_param_groups()
Extra optimizer param groups with custom LR
mixin_on_train_epoch_start()
Per-epoch setup (update schedules, etc.)
Example MRO Chains
DA5CascadeFiLMTopo (low-res)
DiseaseConditioning
→
TopologyLoss
→
ComposableTrainer
→
DA5
→
Trainer
DA5CascadeFullresFiLMTopo (NEW fixed)
DiseaseConditioning
→
TopologyLoss
→
ComposableTrainer
→
DA5
→
Trainer
DA5CascadeTopoScheduled (NEW)
TopologyLossScheduled
→
TopologyLoss
→
ComposableTrainer
→
DA5
→
Trainer
DA5FiLMTopoCurriculum (full-res)
DiseaseConditioning
→
TopologyLoss
→
CurriculumWeights
→
ComposableTrainer
→
DA5

## Slide 10
Trainer Inventory
All 22 composed trainers — low-res, full-res, cascade-fullres stages
10 / 14
Full-Res (3d_fullres)
nnUNetTrainerDA5
Working
Baseline
_100epochs variant available
DA5FiLMV3
Working
DA5 + FiLM bottleneck (K=8)
_100epochs variant available
DA5FiLMTopo
Untested
DA5 + FiLM + clDice
_100epochs variant available
DA5TopoScheduled
New
DA5 + clDice (scheduled)
_100epochs variant available
DA5FiLMTopoCurriculum
Untested
DA5 + FiLM + clDice + Curriculum
_100epochs variant available
Low-Res / Cascade Stage 1 (3d_lowres)
DA5CascadeFiLM
Working
DA5 + FiLM
_100epochs variant available
DA5CascadeTopo
Working
DA5 + clDice (fixed)
_100epochs variant available
DA5CascadeFiLMTopo
Working
DA5 + FiLM + clDice
_100epochs variant available
DA5CascadeTopoScheduled
New
DA5 + clDice (scheduled)
_100epochs variant available
DA5CascadeFiLMAdjacency
Pending
DA5 + FiLM + adjacency
_100epochs variant available
High-Res / Cascade Stage 2 (3d_cascade_fullres)
DA5CascadeFullresBaseline
Working
DA5 only (name wrapper)
_100epochs variant available
DA5CascadeFullresFiLM
Working
DA5 + FiLM
_100epochs variant available
DA5CascadeFullresTopo
Fixed
DA5 + clDice ← FIXED
_100epochs variant available
DA5CascadeFullresFiLMTopo
Fixed
DA5 + FiLM + clDice ← FIXED
_100epochs variant available
DA5CascadeFullresTopoScheduled
New
DA5 + clDice (scheduled)
_100epochs variant available

## Slide 11
Cascade Ablation Experiments
Systematic comparison of FiLM conditioning × topology loss at low-res stage
11 / 14
Exp
Low-res trainer
High-res trainer
FiLM
Topo loss
Mean Dice
AO Dice
PA Dice
Baseline
nnUNetTrainerDA5_100epochs
DA5CascadeFullresBaseline
—
—
—
—
—
A
DA5CascadeFiLM_100epochs
DA5CascadeFullresFiLM
✓
—
—
—
—
B
DA5CascadeFiLMTopo_100epochs
DA5CascadeFullresFiLM
✓
✓
—
—
—
D
DA5CascadeTopo_100epochs
DA5CascadeFullresTopo
—
✓
—
—
—
B+
DA5CascadeFiLMTopo_100epochs
DA5CascadeFullresFiLMTopo
✓
✓
—
—
—
D-S
DA5CascadeTopoScheduled_100epochs
DA5CascadeFullresTopoScheduled
—
✓
—
—
—
NEW/FIXED
FiLM
Topo
Results TBD
B+ and D-S use the newly fixed/created high-res trainers that actually apply topology loss at both stages.
All 100-epoch variants. Use scripts/setup_cascade_predictions.py to create lowres prediction symlinks before training stage 2.

## Slide 12
Contributions — This Implementation Session
Three changes to the codebase
12 / 14
1
TopologyLossScheduledMixin — NEW
variants/mixins/topology_loss.py
◆ Subclasses TopologyLossMixin — inherits all clDice logic
◆ Adds mixin_on_train_epoch_start() to update self.topo_weight each epoch
◆ Uses existing topo_weight_schedule() function (was previously unused)
◆ Schedule: warmup=10 epochs, plateau → decay from epoch 40
◆ Peak weight 0.5 (vs fixed 0.2) — more aggressive topology enforcement at plateau
◆ All schedule params overridable as class attributes in thin subclasses
2
Fixed high-res cascade topology trainers
composed/nnUNetTrainerDA5CascadeFullresVariants.py
◆ DA5CascadeFullresTopo was previously a name-only wrapper around plain DA5
◆ DA5CascadeFullresFiLMTopo was FiLM-only — topology was silently missing
◆ Both now properly use TopologyLossMixin at the high-res stage
◆ Enables end-to-end topology enforcement: low-res (global) + high-res (local)
◆ ⚠ Checkpoints from previous runs with these names are incompatible
3
New scheduled topology composed trainers — NEW
composed/nnUNetTrainerDA5TopoScheduled.py (new file)
◆ DA5TopoScheduled(_100epochs) — full-res with scheduled clDice
◆ DA5CascadeTopoScheduled(_100epochs) — low-res cascade with scheduled clDice
◆ DA5CascadeFullresTopoScheduled(_100epochs) — high-res cascade with scheduled clDice
◆ All follow the same thin composed trainer pattern (~10 lines each)
◆ Pair DA5CascadeTopoScheduled (low-res) + DA5CascadeFullresTopoScheduled (high-res)

## Slide 13
Open Questions & Assumptions
Items to validate before drawing conclusions from experiment results
13 / 14
Q1
Does FiLM actually learn?
Monitor bottleneck_film.weight.abs().mean() during training. γ should diverge from 0 after first few epochs.
Q2
clDice at high-res: local vs global?
High-res patches cover only part of AO/PA. Truncated skeleton may give degraded clDice signal.
Q3
Is topo_w_high = 0.5 too aggressive?
Peak weight 0.5 gives topology ~33% of total gradient. Monitor training loss curves on first scheduled run.
Q4
Memory cost of 10 skeleton iters in 3D?
20 pooling ops per batch (2 classes × 10 iters). Consider num_iter=5 if GPU memory is constrained.
Q5
HLHS / PuA edge cases
Absent/fused vessels → near-empty GT skeleton. Topology loss may mis-penalise correct empty predictions.
Q6
Cascade symlink script coverage
setup_cascade_predictions.py must handle all new trainer name combos (Topo, FiLMTopo, TopoScheduled).
Q7
disease_map.json at cascade-fullres inference
FiLM at high-res stage needs disease vec at inference. Verify predict_disease_conditioned.py handles cascade.
Q8
DA5 augmentation for cardiac CT
Aggressive deformation may be unrealistic for rigid cardiac structures. Compare DA5 vs default augmentation.

## Slide 14
Future Directions
Extensions to explore once training protocol is validated
14 / 14
Per-Disease Topology Exclusion
TopologyLossConditionalMixin: disable clDice for HLHS (flag 0) and PuA (flag 5) cases where AO/PA are absent. Reads disease vector from batch to gate the loss.
Adjacency Loss for VSD/AVSD
DA5CascadeFiLMAdjacency is a placeholder. An adjacency-consistency loss penalising disconnected LV–RV in VSD cases would complement FiLM conditioning.
clDice as Primary Loss
Replace Dice+CE with α·Dice+(1-α)·clDice as the main loss (not extra term). Original paper shows stronger topology preservation. New ClDiceMainLossMixin.
Multi-Stage Encoder FiLM
Apply FiLM at 2 lowest-resolution encoder stages instead of bottleneck-only. Larger receptive field, more spatial context, lower N so (1+γ)^N instability avoided.
Cross-Attention Conditioning
Replace FiLM scale/shift with cross-attention: disease vector attends to spatial bottleneck features. Selective amplification vs. uniform channel rescaling.
Post-Processing: Disease-Aware Largest-CC
Rule-based cleanup: keep N largest connected components per label based on disease flags. Fast, interpretable. TGA/DORV: enforce single AO/PA connected component.